## Slide 1: Sarcoma Group Research Update
April 27, 2021

## Slide 2: Objectives
Review MRI Simulation in Sarcoma
Review chemoradiotherapy and ‘modified Eiber protocol’ in extremity soft tissue sarcoma

## Slide 3: Sarcoma Review
And Rationale for MRI Simulation

## Slide 4: History of Sarcoma
Alexis Boyer (1757-1833) first to distinguish exostosis, gumma of bone, spina ventosa, and osteosarcoma
1891 - First patient with sarcoma cured by immunotherapy, reported 1914 by William B Coley (1862-1936)
1905 - Dr Ernest A Codman (1869-1940) publishes The Use of the X-ray in the Diagnosis of Bone Diseases
Peltier, J Surg Onc 1985; 30:201-205
Notes: Of course, to understand a disease, one must first start at the beginnings
The term osteosarcoma first described in this book
The head and neck sarcoma was probably a melanoma, as back then was classified as a melanosarcoma

## Slide 5: History of Sarcoma
1921 - James Ewing describes diffuse endothelioma of bone (then called Ewing’s tumor by Codman)
1931 - Sir Stanford Cade advocated 6000 rad over six weeks to primary
  If no mets over 6-9 months, then amputate
1941 Ferguson AB: Treatment of osteogenic sarcoma. J Bone Joint Surg 22:92-100, 1940
  “Results indicate that early amputation not only is not the best treatment, but that it actually tends to assure the death of the patient”
  Treatment recommended:
    Avoid early amputation
    Delay amputation
    Give X-ray radiation prior to amputation
    Radiate, excise, and implant bone grafts before amputation
    Repeat excision before amputation
Peltier, J Surg Onc 1985; 30:201-205
Jaffe et al., Sarcoma. 2013; 2013: 203531.
Notes: Even then surgeons were biased that introducing a delay allows for selection between slower and rapidly growing turmors that metastasized early.
Surgery was set back for years based on this recommendations
Survival of 8% of those amputated within 6 months vs 28% of those amputated after 6 months

## Slide 6: Modern Day Treatment
Alektiar, Soft-Tissue Sarcoma, Clinical Radiation Oncology, 2016, p1355

## Slide 7: Sarcoma Epidemiology
~1.5% of adult malignancies
~7.5% of pediatric malignancies
Varied histologies
Primary can arise anywhere
  (really anywhere)
Ferrari et al, Pediatr Blood Cancer 2011;57:943–949
Notes: Based on SEER data

## Slide 8: Distribution of Sarcoma Primary Sites
Ferrari et al, Pediatr Blood Cancer 2011;57:943–949
Chart: 
| H&N | Abdominal | Intrathoracic | Trunk | Extremity | Other
 | 0.10803 | 0.20187 | 0.026851 | 0.21408 | 0.31903 | 0.13
Notes: Extremeties

## Slide 9: Sarcoma Volume Delineation
GTV
CTV
PTV

## Slide 10: ‘Classical’ Sarcoma Planning
Murphey MD, Robbin MR, Mcrae GA et-al. The many faces of osteosarcoma. Radiographics. 17 (5): 1205-31.

## Slide 11: Conventional Margins
Alektiar, Soft-Tissue Sarcoma, Clinical Radiation Oncology, 2016, p1359-1360
Notes: Conceptually, for preoperative radiation, this is how it used to be done. About 5cm to block from GTV
Talk about pseudocapsule of tumor
Note CTV is trimmed from uninvolved fascial compartments

## Slide 12: Radiation Clinical Trials in Sarcoma

## Slide 13: Preoperative Versus Postoperative RT
NCIC SR2
Notes: SR2 - Randomized 190 patients stratified by tumor size (<10cm > 10cm) to 50 Gy preop vs 66-7- Gy postop)
1994-1997

## Slide 14: NCIC SR2 Results
Equivalent LC and OS between preoperative and postoperative groups
Higher incidence acute wound complications in preoperative
Postoperative group had trend towards increased late toxicity at 2 years (p=0.07) of
  Subcutaneous fibrosis
  Joint stiffness
  Edema
Notes: Long term toxicity correlated with decreased disability

## Slide 15: NCIC SR2 Results
Larger Field size risk factor for:
  Subcutaneous fibrosis
  Joint stiffness
  Edema
Confounding variables:
  Larger field sizes post operatively
  Dmax higher postoperatively
Notes: Long term toxicity correlated with decreased disability

## Slide 16: Technology Advances in Sarcoma Care:
Better diagnostic imaging/proper staging
Transition from 2D to 3D-CRT and then IMRT radiotherapy
Improvements in onboard imaging and IGRT
Desire to reduce treatment toxicity
Notes: Will Rogers was an early century comedian, not actually a significant contributor to STS treatment. But modern DI does absolutely play a role.

## Slide 17
Notes: Phase II RTOG trial with preoperative radiotherapy with daily IGRT to assess impact of margin reduction

## Slide 18: RTOG 0630 Treatment
Daily IGRT
  PTV margin now +0.5 cm instead of +1.0 cm
CTV Margins
  Instead of +4 cm longitudinally, 1.5cm radially
    G2/G3 histology, 8 cm tumor length
      +3.0cm longitudinal expansion, +1.5cm radially
    G1 histology, <8cm tumor length
      +2.0cm longitudinal expansion, +1.0cm radially

## Slide 19: RTOG 0630 Results
Notes: In the paper, at least one of the in field recurrences the GTV was not adequately covered when compared to the MRI
These failure differences are using the same definitions of SR2

## Slide 20: RTOG 0630 and NCIC SR2 Comparisons
57 of 79 patients were compared at the same 2 year late toxicity endpoint as in SR2
6/57 (10.5%) had ≥G2 late toxicities in 0630 compared to 27/73 (37%) in SR2 (P<0.001)
SR2 LC5 = 93% vs 0630 LC4 = 93%
Notes: Will all the caveats that come with direct trial comparisons…
No marginal field recurrences

## Slide 21: RTOG 0630 Conclusions:
Smaller field sizes enabled by IGRT contribute to
  Less late toxicity
  Similar local control

## Slide 22: Workflow for PTV Creation
GTV
CTV
PTV
  Reduction based on RTOG 0630
  Reduction based on setup, IGRT
  Can we make this more accurate?

## Slide 23: GTV Delineation
CT sim alone not enough for disease delineation given soft tissue nature
MRI shows limits of sarcoma involvement much more accurately
Errors in GTV delineation are introduced from registration of diagnostic scans to simulation scans
Vickers et al., BJR 2019; 1: 20180022.
Kransdorf et al., AJR 2000;175: 575-587
Notes: There is evidence showing MRI fusion planned preoperative sarcoma radiotherapy plans results in GTV shrinkage by ~21cc on average. Small, but helps.

## Slide 24: Sarcoma Imaging
Notes: Top left – CT Sim
Top right – T2 Fat Sat MRI Sim
Bottom left – T1 + Gad MRI Sim
Bottom right – T1 + Gad Diagnostic MRI – fortunately, in this circumstance there is a good match with the surface contour.
Sometime PET is used depending on the situation
Great quality on the Gad+contrast scan!!

## Slide 25: Diagnostic to Simulation Registration Errors
Time delay from diagnostic imaging to simulation imaging
  Can be upwards of month or more time interval, where tumor has opportunity to grow and invade and may result in undercontouring of tumor
Diagnostic positioning varies greatly from treatment positioning
  Extremities by nature, have large degrees of freedom of movement due to joints
  Even if external contours are similar, muscle (and therefore sarcoma) positioning vary and therefore are not reliable
Notes: Most importantly is variations in anatomical positioning

## Slide 26
Allen Li et al., Pract Radiat Oncol. 2016 Jul-Aug; 6(4): e135–e140
Notes: That difference is greater than the sum total distance gained with IGRT ( based on secondary analysis of RTOG 0630 – need 1.5cm CTV to PTV expansion to account for day to day variation)

## Slide 27
IFS measurement difference between S1 and S2 was 11.8mm (CI 9.9 to 13.7 mm, p<0.001)
Daily IGRT only allows reduction of 5-10mm from 15 mm PTV
Allen Li et al., Pract Radiat Oncol. 2016 Jul-Aug; 6(4): e135–e140
Notes: That difference is greater than the sum total distance gained with IGRT ( based on secondary analysis of RTOG 0630 – need 1.5cm CTV to PTV expansion to account for day to day variation)

## Slide 28: A brief note on image registration
AAPM TG-132 (2017) describes image registration, fusion algorithms and techniques
Potential exists for deformable registration techniques, but with increased degrees of freedom, there is increased potential for error
At present, routine registrations are rigid
Brock, et al. Use of image registration and fusion algorithms and techniques in radiotherapy: Report of the AAPM Radiation Therapy Committee Task Group No. 132

## Slide 29: Registration methods
Brock, et al. Use of image registration and fusion algorithms and techniques in radiotherapy: Report of the AAPM Radiation Therapy Committee Task Group No. 132

## Slide 30: Fellowship Project
Notes: LC0036932
RV5498832

## Slide 31: Extremity MRI Simulation

## Slide 32: Hypothesis
More precise CTV delineation can be created with the use of MRI simulation
This in turn should be result in reduced toxicity for patients without reduction in local control
Notes: Newer technology and has its challenges, so not as well described in literature
Objective of my work was to work with Ives, Sim Techs to help introduce the implementation here at MUHC

## Slide 33: Project: Implementing MRI Sim for Sarcoma at MUHC
Primary objective is to develop set of protocols and experience for extremity sarcoma
Diagnostic MRI protocols exist for extremities and other anatomical areas where sarcomas arise, however
Cannot translate diagnostic protocols to treatment protocols 1:1 as there are limitations on both the MRI acquisition and treatment delivery

## Slide 34: Image Acquisition
CT Sim is done first (45min)
  +- bolus as needed (usually wet towel)
  No contrast at this step
  Skin markers for incisions, biopsy sites, drains as needed
  Vac loc for most cases
MRI Sim is done second (45min, usually same day)
  Patient placed in same positioning on MR Sim bed
  Commercial skin markers used as above
  Receiver coils placed over anatomical site of interest
  Scans acquired with IV contrast (gadolinium)

## Slide 35: Receiver Coil
High RF sensitivity over a small region of interest
Placed over the anatomy of interest

## Slide 36: MRI Sequences
Scout scan done first with low fidelity to plan simulation scans
  Verifies treatment position
  Verifies image quality with receiver coils
  Delineate limits for field of view, orientation of scan, motion artifact, and shim
  Parameters are selected so each scan is no longer than about 7 min
    This depends on slice thickness, if there are limitations on energy deposition due to surgical hardware, stents, etc.
3 scans acquired
  Axial T2 fat saturated
  Axial T1 + contrast
  Coronal T2 fat saturated
Notes: Found coronals more helpful than sagitals. The eclipse upgrade does enable contouring on sagittal and coronal views, so from a workflow perspective that may change in the future, but for now, this is what we’ve found to be most helpful

## Slide 37: Sample MRI Parameter Card
Notes: Describes what is needed for scan parameters
Shim…
These are defined for our MRI sims

## Slide 38: Logistical Considerations
Can’t really do ‘add-ons’
Need:
  MRI consent
  Verification of any MR compatible hardware, stents, etc.
  MRI sim staff available
  MRI sim time available
Many sarcoma consults were from outside Montreal, so lead time can limit ability for distant patients to arrange, as opposed to a same day add-on CT Sim
  Largest barrier to access to date

## Slide 39: Sarcoma Sites Imaged
Lower extremity
  Thigh
  Knee
  Calf
Pelvic
  Iliac crest
  Vulvar
Forearm
Cervical spine

## Slide 40: Challenges with MRI Sim
Both technical and logistical
Sarcoma also difficult from treatment planning and delivery perspective even without added complexity of MRI simulation

## Slide 41: MRI Technical Challenges
Patient positioning in MRI limited from bore size, restriction of receiver coil
Field of View (FoV) limit in MRI due to limitations of shim, receiver coils, and scan lengths
  Large FoV scans will require:
    Two sets of images (eg inferior and superior)
    ~Twice the MRI time to acquire
    Other protocols working around this limitation were a work in progress
For best image acquisition, target should be as closest to centre of bore as possible
  This is DIFFERENT than vast majority of treatment positions, hence the challenge

## Slide 42: MRI Technical Challenges
Chest wall lesions have respiratory motion
Upper extremity lesions have no good obvious way to position in centre of magnet that is also treatable

## Slide 43: Treatment Challenges
Limited on leg positioning due to limitations of MRI
  Potential of increasing dose by proximity to contralateral limb
  May limit how bolus is positioned, but usually this is flexible

## Slide 44: MRI Simulator Sarcoma Cases

## Slide 45: Demographics
10 patients, 12 plans
5 lower extremity
2 upper extremity
2 pelvis
1 spine

## Slide 46: Cases Performed
Intent | 
Preoperative | 7
Postoperative | 1
Oligomet | 1
Palliative | 1
Location | 
Leg | 5
Arm | 2
Pelvis | 2
Spine | 1
Histology | 
Myxofibrosarcoma | 3
Undifferentiated pleiomorphic sarcoma | 2
Leiomyosarcoma | 1
Liposarcoma | 2
Epithelioid | 1
Ewing Sarcoma | 1

## Slide 47: Preoperative RT: High Grade Myxoid/Round Cell Liposarcoma
Notes: Patient underwent MRI simulation, Contour shows gross tumor + surrounding edematous changes

## Slide 48: Preoperative RT: High Grade Myxoid/Round Cell Liposarcoma
Notes: Patient underwent MRI simulation, Contour shows gross tumor + surrounding edematous changes

## Slide 49: Importance of Recent MRI
Notes: Diagnostic MRI performed September 13

## Slide 50: Importance of Recent MRI
Notes: Diagnostic MRI performed September 13

## Slide 51: Preoperative RT Post Unplanned Excision: High Grade Myxofibrosarcoma

## Slide 52: Preoperative RT Post Unplanned Excision: High Grade Myxofibrosarcoma

## Slide 53: Preoperative RT Post Unplanned Excision: High Grade Myxofibrosarcoma
Notes: This is the diagnostic MRI - > even with fusion, compared to sim -> off by ~1.5cm root mean distance from centroid!
Note change in body surface anatomy as well

## Slide 54: Preoperative RT Post Unplanned Excision: High Grade Myxofibrosarcoma
Notes: Can see mismatch in thorax well – required separate position for upper extremity MR sim -> was not perfect fusion

## Slide 55: Preoperative RT Post Unplanned Excision: Vulvar Epithelioid Sarcoma

## Slide 56: Preoperative RT Post Unplanned Excision: Vulvar Epithelioid Sarcoma

## Slide 57: SBRT for Oligometastatic Leiomyosarcoma
Notes: Lesion was picked up on followup PET. NOT seen on CT Sim, OR CT component of PET.
Can you identify the lesion?

## Slide 58: SBRT for Oligometastatic Leiomyosarcoma
Notes: Lesion was picked up on followup PET. NOT seen on CT Sim, OR CT component of PET.
In crosshairs, outlined in blue. Not visible otherwise!!
Note AP direction of motion artifact due to bowel- would have been helpful to give buscopan in this case, however, still worked

## Slide 59: SBRT for Oligometastatic Leiomyosarcoma
Notes: Same case… retrospectively had bone lesion as well identified on diagnostic MRI done for other purpose, week after MR sim was done. Not PET avid! However suspicious on MRI. Well, luckily enough we see it here. Again, not obvious on CT but in retrospect visible

## Slide 60: SBRT for Oligometastatic Leiomyosarcoma
Notes: Here is the MRI Sim image

## Slide 61: SBRT for Ewing Sarcoma
Notes: 9 year old female with ewing sarcoma, retreatment at sensitive site. MRI used for accuracy

## Slide 62: SBRT for Ewing Sarcoma
Notes: MRI spine not new per say but successful

## Slide 63: Results
Chart: Median Absolute Volume Changes and Ranges
| Median (cm3)
CTV volume difference (absolute) | 16.505
PTV-5mm volume difference (absolute) | 35.25
PTV-7mm volume difference (absolute) | 38.42
Notes: Overall mean differences were low. Large variance

## Slide 64: Results
Chart: Median Relative Volume Changes and Ranges
| Median (cm3)
CTV volume difference (relative) | 0.03
PTV-5mm volume difference (relative) | 0.12
PTV-7mm volume difference (relative) | 0.15

## Slide 65: Results
Chart: Median Sorensen-Dice Coefficients and 95% CI
| Median
CTV Sørensen-Dice coefficient | 0.73446
PTV-3mm Sørensen-Dice coefficient | 0.73018
PTV-5mm Sørensen-Dice coefficient | 0.79149
PTV-8mm Sørensen-Dice coefficient | 0.8142
PTV-8mm Sørensen-Dice coefficient | 0.76451
Notes: Overall a high degree of overlaps. Overlaps become less significant with larger PTVs.

## Slide 66: Results
Largest differences in Sørensen-Dice coefficients were observed in upper extremities and hips
Sørensen-Dice coefficients were also low in SBRT plans due to low absolute treatment volumes

## Slide 67: Conclusions
Extremity STS has a wide anatomical variation from diagnostic imaging to treatment position
MRI simulation may help reduce registration errors and aid in defining GTV and CTV in extremity soft tissue sarcoma
  This may help in turn reduce treatment volumes and patient toxicity
MRI simulation allows for routine lower extremities fusions
  Upper extremities have their own challenges and will need team based approach

## Slide 68: ‘Modified Eiber Protocol’